## Slide 1: Digital Signal Processing Introduction
CPSC 501: Advanced Programming Techniques
Fall 2020
Jonathan Hudson, Ph.D
Instructor
Department of Computer Science
University of Calgary
Tuesday, September 22, 2020

## Slide 2: Signals
How to we get a signal

## Slide 3: Analog Signal
Analog signal. This signal v(t)=cos(2πft) could be a perfect analog recording of a pure tone of frequency f=1 Hz.
The period T=1/f is the duration of one full oscillation.

## Slide 4: Noisy Signal
Noisy analog signal. Noise degrades the sinusoidal signal.
It is often impossible to recover the original signal exactly from the noisy version

## Slide 5: Digital Signal
Analog transmission of a digital signal.
Consider a digital signal 100110 converted to an analog signal for radio transmission.
The received signal suffers from noise, but given sufficient bit duration , it is still easy to read off the original sequence 100110 perfectly.

## Slide 6: Sampling
A continuous signal may be sampled
  i.e. measured periodically at small intervals of time, and converted into a series of numbers (samples)
    Such a series is a digital signal
  An analog-to-digital converter does the sampling
    E.g. Sampling an audio signal

## Slide 7: From Voice to Bits
How to we get a signal

## Slide 8: Original Signal

## Slide 9: Analog Signal: Via Transducer

## Slide 10: Analog Signal Cleaning

## Slide 11: Analog to Digital

## Slide 12: And back again

## Slide 13: Sampling and Quantization
A digital-to-analog converter converts the digital signal back into an analog signal

## Slide 14: Sampling

## Slide 15: Sampling
Sampling is the process of recording an analog signal at regular discrete moments of time.
The sampling rate is the number of samples per second.
The time interval between samples is called the sampling interval .

## Slide 16: Original signal
The signal v(t)=cos(2πft) is sampled uniformly with 3 sampling intervals within each signal period T.
Therefore, the sampling interval T/3 and the sampling rate 3f.
Notice that there are three samples in every signal period T.

## Slide 17: Sample points
To express the samples of the analog signal x, we will use the notation x[n] for example
  integer values of n index the samples
Typically, the n=0 sample is taken from t=0
Consequently, the n=1 sample must come from the time point, exactly one sampling interval later; and so on.
sequence of samples can be written as

## Slide 18: Store sample: extracted from formula
for integer n
Our signal was
as

## Slide 19: Stored sample: if measured
-0.5
-0.5

## Slide 20: Can we rebuild it?
-0.5
-0.5

## Slide 21: Sampling rate

## Slide 22: Higher rate sampling
Sampling at a high rate.
The signal v(t)=cos(2πft) is sampled uniformly with 12 sampling intervals within each signal period T.
The sampling interval and the sampling rate .
The original signal x(t) can be recovered from the samples by connecting them together smoothly.

## Slide 23: Lower rate sampling
In contrast, if a sinusoidal signal is sampled with a low sampling rate, the samples may be too infrequent to recover the original signal.

## Slide 24: Best sample rate
Sampling a cosine at .
The signal v(t)=cos(2πft) is sampled uniformly with 2 sampling intervals within each signal period T.
sampling interval and the sampling rate .
sample at every peak/trough of the sinusoid, there is no lower frequency sinusoid that fits these samples.
x(t) can be recovered exactly from the samples by ideal low pass filtering.

## Slide 25: Worst case sample rate
The signal sin(2πft) is sampled uniformly with 2 sampling intervals within each signal period T.
Since all the samples are at the zero crossings, ideal low pass filtering produces a zero signal instead of recovering the sinusoid.

## Slide 26: So how do we decide sample rate

## Slide 27: Nyquist-Shannon theorem
The Nyquist-Shannon sampling theorem
  The sampling rate for exact recovery of a signal composed of a sum of sinusoids is larger than twice the maximum frequency of the signal.
  This rate is called the Nyquist sampling rate

## Slide 28: Terminology reminder
Sampling is the process of recording an analog signal at regular discrete moments of time.
The sampling rate is the number of samples per second.
The time interval between samples is called the sampling interval .

## Slide 29: Theroem basics
The sampling theorem:
  The sampling frequency must be greater than twice the bandwidth of the signal in order to recreate it perfectly
    fh < R/2, where fh is the frequency of the highest component of the signal, and R is the sampling rate
  If you sample at too low a rate, aliasing or foldover distortion results

## Slide 30: Details

## Slide 31: Sampling and Quantization

## Slide 32: Sampling and Quantization
The frequency of the alias is calculated with:

## Slide 33: Example
The frequency of the alias is calculated with:
  If F = 25000 Hz, and R = 30000 Hz

## Slide 34: Example (cont’d)
The frequency of the alias is calculated with:
  If F = 25000 Hz, and R = 30000 Hz

## Slide 35: Example (cont’d)
The frequency of the alias is calculated with:
  If F = 25000 Hz, and R = 30000 Hz
  when k =1

## Slide 36: Example (cont’d)
The frequency of the alias is calculated with:
  If F = 25000 Hz, and R = 30000 Hz, then k = 1
  when k =1

## Slide 37: Low-pass filtering
  To avoid aliasing, the signal is low-pass ﬁltered before A/D conversion, eliminating any frequency components above R/2

## Slide 38: More information

## Slide 39: Some rates used
  Common audio sample rates:
    CD: 44.1 kHz
      Note: range of human hearing is 20 Hz to 20 kHz
  Pro audio: 48 kHz, 96 kHz, 192 kHz
  Speech codecs: 8000 Hz
  Apple lossless (maximum 384 kHz)
  Streaming music 44.1 kHz (some of this limit is contractual)

## Slide 40: Digital form?
The A/D converter quantizes the instantaneous amplitude of each sample
  i.e. represents it using N-bit binary number
    Normally a signed integer
  The more bits the better, to improve the signal-to-noise ratio
    E.g. 16 bits gives SNR of about 96 dB

## Slide 41: Commons sample bit sizes
  Common sample sizes:
    CD/Stream: 16-bit
    Pro audio (subscriber streams): 20-bit, 24-bit
    Speech codecs: 8-bit, 12-bit

## Slide 42: Onward to … spectral analysis.
Jonathan Hudson
jwhudson@ucalgary.ca
https://pages.cpsc.ucalgary.ca/~hudsonj/