## Slide 1: Digital Signal Processing: Spectral Analysis
CPSC 501: Advanced Programming Techniques
Fall 2020
Jonathan Hudson, Ph.D
Instructor
Department of Computer Science
University of Calgary
Monday, August 24, 2020

## Slide 2: Fourier Theorem

## Slide 3: Fourier Theorem
Fourier Theorem:
  Any continuous, periodic waveform can be expressed as the sum of a series of sine and cosine terms, each having speciﬁc amplitude and phase coefﬁcients
  Any physical function that varies periodically with time with a frequency f can be expressed as a superposition of sinusoidal components of frequencies: "

## Slide 4: Additive synthesis
Pure tones can be added together to form a complex tone (additive synthesis):

## Slide 5: Fourier decomposition
Fourier analysis decomposes a complex signal into its component parts
  i.e. its spectrum
  The Fourier transform calculates the spectrum of a continuous signal
    Transforms from the time domain to the frequency domain

## Slide 6: Discrete Fourier Transform

## Slide 7: Discrete Fourier Transform
The discrete Fourier transform (DFT) calculates the spectrum of a digital signal
  Deﬁnition:
    N is the number of samples per period of the waveform
    k is the harmonic number
    and ω = 2π/N

## Slide 8: What frequencies are present
The discrete Fourier transform (DFT) calculates the spectrum of a digital signal
Spectrum -> Which frequencies are present
Harmonic Numbers -> we go up multiples of frequencies (this gives us regular components to break signal down into)

## Slide 9: Breakdown
Since , can be expressed as:
We must calculate the real part and the imaginary part separately
Real part
Imaginary part

## Slide 10: In code

## Slide 11: Get initial summation values
C implementation:
      #define PI 3.141592653589793
      #define TWO_PI (2.0 * PI)
      void dft(double x[], int N, double a[], double b[]){
      int n, k;
      double omega = TWO_PI / (double)N;
      for (k = 0; k < N; k++) {
      a[k] = b[k] = 0.0;
      for (n = 0; n < N; n++) {
      a[k] += (x[n] * cos(omega * n * k));
      b[k] -= (x[n] * sin(omega * n * k));
      } } }

## Slide 12: Process result
The results must be further processed :
  and must be scaled by N:
      for (k = 0; k < N; k++) {
      a[k] /= (double)N;
      b[k] /= (double)N;
      }
  The magnitude or amplitude |X(k)| is given by:
      for (k = 0; k < N; k++)
      amplitude[k] = sqrt( (a[k] * a[k]) + (b[k] * b[k]) )

## Slide 13: What we get?

## Slide 14: Harmonic numbers
The DFT gives amplitudes for both positive and negative frequencies (harmonics)
  If N = 8:

## Slide 15: Final amplitudes
Add these together to get the amplitude of a harmonic:
    x[0] = amplitude[0];
    x[N/2] = amplitude[N/2];
    for (k = 1, j = N-1; k < N/2; k++, j--)
      x[k] = amplitude[k] + amplitude[j];

## Slide 16: Performance?

## Slide 17: Performance
The DFT is
  Not practical for large data sets
  Can be calculated more efﬁciently with the fast Fourier transform (FFT)
    Is O(N log N)
There are many variants of the FFT
  Most work by reordering the data, and then recursively subdividing it in half
    Thus data size must be a power of 2
Most FFTs work with complex numbers
  The signal is the real part
  The imaginary part is set to 0
  This data is packed into an array of size*2:

## Slide 18: FFT

## Slide 19: Spectral Analysis

## Slide 20: Spectral Analysis
Like the DFT, the output of the FFT must be further processed to give meaningful results
The DFT calculates the spectrum for a single cycle of a waveform
  Result can be displayed as a bar graph
  Shows the relative amplitudes of the harmonics

## Slide 21: Signals as frequency bar graphs

## Slide 22: DFT Window
The DFT can be applied to an arbitrary “window” of a longer waveform
  Is a “snapshot” of the spectrum at a particular time
  Window is typically 512 or 1024 samples long
  Instead of harmonics, the output represents how much energy is present in particular “bins”
    When graphed, the amplitudes are joined together to form a continuous line
    E.g.

## Slide 23: Example frequency outputs

## Slide 24: Within an application

## Slide 25: Spectral Analysis
The spectrum can be plotted as it changes over time
  The analysis window slides along the time axis
    Can be end to end
    Or overlapping
  Can be graphed as a 3D “waterfall”
    E.g.

## Slide 26: Spectral Analysis

## Slide 27: Spectral Analysis
Can also be displayed as a spectrogram
  X axis: time
  Y axis: frequency
  Darkness of pixel represents amplitude
    White: 0 amplitude
    Black: full amplitude
  E.g.

## Slide 28: Spectral Analysis

## Slide 29: Spectral Analysis

## Slide 30: Spectral Analysis

## Slide 31: Onward to … convolution.
Jonathan Hudson
jwhudson@ucalgary.ca
https://pages.cpsc.ucalgary.ca/~hudsonj/