## Slide 1: Transmission Media
CPSC 441 Tutorial – April 2, 2012
TA: Ruiting zhou

## Slide 2: Residential access: cable modems
Does not use telephone infrastructure
  Instead uses cable TV infrastructure
  It is integrated into the cable TV infrastructure analogously to DSL which uses the existing telephone network.
  DSL: Digital subscriber line, provide internet access by transmitting digital data over the wires of a local telephone network
HFC: hybrid fiber coax
  Asymmetric: up to 30 Mbps downstream, 2 Mbps upstream
network of cable and fiber attaches homes to ISP router
  homes share access to router
  unlike DSL, which has dedicated access

## Slide 3: Residential access: cable modems
tap, a device that monitors data on a computer network

## Slide 4: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)
Typically 500 to 5,000 homes

## Slide 5: Cable Network Architecture: Overview
home
cable headend
cable distribution
network
server(s)

## Slide 6: Cable Network Architecture: Overview
home
cable headend
cable distribution
network (simplified)

## Slide 7: Cable Network Architecture: Overview
home
cable headend
cable distribution
network
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
FDM Frequency-division multiplexing
(more shortly):

## Slide 8: Fiber to the Home
ONT
OLT
central office
optical
splitter
ONT
ONT
optical fiber
optical fibers
Internet
Optical links from central office to the home
Two competing optical technologies:
  Passive Optical network (PON) : uses electrically powered switching equipment, such as a router or a switch aggregator, to manage signal distribution and direct signals to specific customers
  Active Optical Network (AON): uses optical splitters to separate and collect optical signals as they move through the network
Much higher Internet rates; fiber also carries television and phone services

## Slide 9: Home networks
Typical home network components:
DSL or cable modem
router/firewall/NAT
Ethernet
wireless access point
wireless
access
point
wireless
laptops
router/
firewall
cable
modem
to/from
cable
headend
Ethernet

## Slide 10: Physical Media
Bit: propagates between transmitter/rcvr pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
Twisted Pair (TP)
two insulated copper wires
  Category 3: traditional phone wires, 10 Mbps Ethernet
  Category 5: 100 Mbps Ethernet

## Slide 11: Physical Media: coax, fiber
Coaxial cable:
two concentric copper conductors
bidirectional
baseband:
  single channel on cable
  legacy Ethernet
broadband:
  multiple channels on cable
  HFC
Fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 10’s-100’s Gbps)
low error rate: repeaters spaced far apart ; immune to electromagnetic noise

## Slide 12: Physical media: radio
signal carried in electromagnetic spectrum
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
Radio link types:
terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., WiFi)
  11 Mbps, 54 Mbps
wide-area (e.g., cellular)
  3G cellular: ~ 1 Mbps
satellite
  Kbps to 45 Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus low altitude

## Slide 13: Analog and Digital Transmissions
use of both analog and digital transmissions for a computer to computer call. Conversion is done by the modems and codecs.

## Slide 14: Data Encoding Techniques
Digital Data, Analog Signals [modem]
Digital Data, Digital Signals [wired LAN]
Analog Data, Digital Signals [codec]
  Frequency Division Multiplexing (FDM)
  Wave Division Multiplexing (WDM) [fiber]
  Time Division Multiplexing (TDM)
  Pulse Code Modulation (PCM) [T1]
  Delta Modulation

## Slide 15: Digital Data, Digital Signals [the technique used in a number of LANs]
Digital signal – is a sequence of discrete, discontinuous voltage pulses.
Bit duration : the time it takes for the transmitter to emit the bit.
Issues
  Bit timing
  Recovery from signal
  Noise immunity

## Slide 16: Binary Encoding
NRZ (non-return to zero)
NRZI (NRZ inverted)
Manchester (used by IEEE 802.3, 10 Mbps Ethernet)

## Slide 17: Non-Return to Zero (NRZ)
Encode binary data onto signals
  e.g., 0 as low signal and 1 as high signal
  voltage does not return to zero between bits
    known as Non-Return to Zero (NRZ)
Bits
NRZ
0
0
1
0
1
1
1
1
0
1
0
0
0
0
1
0

## Slide 18: Problem: Consecutive 1s or 0s
Low signal (0) may be interpreted as no signal
High signal (1) leads to baseline wander
Unable to recover clock
  sender’s and receiver’s clock have to be precisely synchronized
  receiver resynchronizes on each signal transition
  clock drift in long periods without transition
sender’s clock
receiver’s clock

## Slide 19: NRZI
Non-Return to Zero Inverted (NRZI)
has a transition at a clock boundary if the bit being transmitted is “1”
Stay at current signal (maintain voltage level) to encode/ transmit a “zero”
Solves the problem of consecutive ones (shifts to 0s)
NRZI can have long series of zeros , still unable to recover clock

## Slide 20: Manchester
Manchester (in IEEE 802.3 – 10 Mbps Ethernet)
Split cycle into two parts
  Send high--low for “1”, low--high for “0”
  Transmit XOR of NRZ encoded data and the clock
Clock signal can be recovered from the encoded data.
Only 50% efficient (1/2 bit per transition): double the transmission rate.

## Slide 21: Different Encoding Schemes
Bits
NRZ
Clock
Manchester
NRZI
0
0
1
0
1
1
1
1
0
1
0
0
0
0
1
0

## Slide 22: Reference
CPSC 441 Chapter 1 Slides 16-28
http://en.wikipedia.org/wiki/File:NRZI_example.png
CS716 Advanced Computer Networks by Dr. Amir Qayyum