## Slide 1: Transmission Media
CPSC 441
TA: Fang WANG
Part of the slides are from Sudhanshu Kumar etc at slideshare.net

## Slide 2: Characteristics
A good transmission medium should provide communication with good quality at long distance.
For voice communication, quality of communication is determined by the voice quality.
For data communication, however, the quality of communication is mainly determined by the effective data rate of communication.

## Slide 3
Transmission Media
Guided Media
Twisted Pair Cable
Coaxial Cable
Unguided Media
Radio
Fiber-Optic Cable
Microwave
Satellite

## Slide 4: Overview
Guided transmission media – wire (twisted pair, cable, fiber)
Unguided – wireless (radio wave, microwave, satellite)
Characteristics and quality determined by medium and signal
For guided, the medium is more important
For unguided, the bandwidth produced by the antenna is more important
Key concerns are data rate and distance

## Slide 5: Design Factors
Bandwidth
  Higher bandwidth gives higher data rate
Transmission impairments
  Attenuation
  Distortion during signal propagation
  Noises
Interference
Number of receivers
  In guided media
  More receivers (multi-point) introduce more attenuation (need more amplifies or repeaters)

## Slide 6: Electromagnetic Spectrum

## Slide 7: Guided Transmission Media
Twisted Pair
Coaxial cable
Optical fiber

## Slide 8: Twisted Pair

## Slide 9: Twisted Pair - Applications
Most common medium
Telephone network
  Between house and local exchange (subscriber loop)
Within buildings
  To private branch exchange
For local area networks (LAN)
  10Mbps or 100Mbps

## Slide 10: Twisted Pair - Pros and Cons
Cheap
Easy to work with
Low data rate
Short range

## Slide 11: Twisted Pair - Transmission Characteristics
Analog
  Amplifiers every 5km to 6km
Digital
  Use either analog or digital signals
  repeater every 2km or 3km
Limited distance
Limited bandwidth (1MHz)
Limited data rate (100MHz)
Susceptible to interference and noise

## Slide 12: Performance
One way to measure the performance of twisted pair cable is to compare attenuation versus frequency and distance.
Gauge is a measure of the thickness of the wire.

## Slide 13: Coaxial Cable

## Slide 14: Coaxial Cable Applications
Most versatile medium
Television distribution
  Cable TV
Long distance telephone transmission
  Can carry 10,000 voice calls simultaneously
  Being replaced by fiber optic
Short distance computer systems links
Local area networks

## Slide 15: Coaxial Cable - Transmission Characteristics
Analog
  Amplifiers every few km
  Closer if higher frequency
  Up to 500MHz
Digital
  Repeater every 1km
  Closer for higher data rates

## Slide 16: Performance
The performance is similar to the twisted pair cable.
The only difference is that the attenuation is much higher in co-axial cable than in twisted pair cable.

## Slide 17: Optical Fiber

## Slide 18: Optical Fiber - Benefits
Greater capacity
  Data rates of hundreds of Gbps
Smaller size & weight
Lower attenuation
Electromagnetic isolation
Greater repeater spacing
  10s of km at least

## Slide 19: Optical Fiber - Applications
Long-haul trunks
Metropolitan trunks
Rural exchange trunks
Subscriber loops
LANs

## Slide 20: Optical Fiber - Transmission Characteristics
Act as wave guide for 1014 to 1015 Hz
  Portions of infrared and visible spectrum
Light Emitting Diode (LED)
  Cheaper
  Wider operating temp range
  Last longer
Injection Laser Diode (ILD)
  More efficient
  Greater data rate
Wavelength Division Multiplexing

## Slide 21: Performance
The performance can be measured by plot of attenuation versus wavelength.
Attenuation is flatter than in case of twisted pair cable and co-axial cable.

## Slide 22: SOME BASIC DIFFERENCES --Twisted Wire
It is inexpensive and already is in use.
Twisted wires are slow, high-speed transmission causes interference (crosstalk).
Limiting factors: skin effect & radiation effect.

## Slide 23: SOME BASIC DIFFERENCES -- Coaxial Cable
It is often used in place of twisted wire for important links in a network because it is faster.
More interference-free transmission medium (speed: 200 megabits per second).
Coaxial cable is thick, is hard to wire in many buildings. It does not support analog conversations.

## Slide 24: SOME BASIC DIFFERENCES -- Optical Fiber
Optical fibers are faster, lighter, and suitable for transferring large amount of data.
Fiber-optic cable is more difficult to work with, more expensive.
Its difficult to install them.

## Slide 25: Unguided Media
Unguided media is still ‘media’ (stuff that signal travels though). The trick is that the media is usually not directional, like air, space, etc. Because the effect is usually much wider than with guided media, there have been a lot of regulation, licensing, and standardization of transmissions via unguided media.

## Slide 26: Wireless Transmission
Wireless transmission that sends signals through air or space without any physical wire.
Common uses of wireless data transmission include pagers, cellular telephones, microwave transmissions, communication satellites, mobile data networks, personal digital assistants, television remote controls.

## Slide 27: Radio Waves
Although there is no clear cut demarcation between radio waves and microwaves , electromagnetic waves ranging in frequencies between 3KHz and 1GHz normally called radio waves.
Radio waves are omnidirectional.
Radio waves particularly those waves that propagate in the sky mode , can travel long distances .This makes Radio waves a good candidate for long distance broadcasting such as AM Radio

## Slide 28: Applications
The omnidirectional characteristics of Radio waves make them useful for multicasting, in which there is one sender but many receivers.
AM and FM Radio, television ,maritime radio , cordless phone , and paging are examples of multicasting.

## Slide 29: Microwaves
Electromagnetic waves having frequency between 1 and 300 GHz are called as Micro waves.
Micro waves are unidirectional.
Microwave propagation is line of sight.
Very high frequency Micro waves can not penetrate walls.
The microwave band is relatively wide, almost 299 GHz

## Slide 30: Applications
Microwaves due to their unidirectional properties are very useful when unicast (one to one ) communication is needed between the sender and the receiver.
They are used in Cellular phones, satellite networks and wireless LANs.

## Slide 31: Infrared Waves
Infrared waves , with frequencies from 300GHz-400THz can be used for short range communication
Infrared waves having high frequencies can not penetrate walls.
When we use our Infrared control , we do not interfere with use of the remote by our neighbors.
We cannot use Infrared waves outside a building because the suns rays Contain Infrared waves that can interfere with communication.

## Slide 32: Applications
The infrared band almost 400 THz has an excellent potential for data transmission.
Such a wide bandwidth can be used to transmit digital data with a very high data rate.
Infrared waves is used in communication between devices such as Keyboard, PCs and Printers.

## Slide 33: Reference
Transmission media ppt, Sudhanshu Kumar etc at slideshare.net
Chapter 4, Transmission Media slides, William Stallings, Data and Computer Communications 7th Edition