## Slide 1: The Internet Protocol
CPSC 441 Tutorial
TA: Fang Wang
Some of the slide contents are courtesy of the authors of the the following textbooks:
- “Mastering Computer Networks: An Internet Lab Manual”, J. Liebeherr, M. El Zarki, Addison-Wesley, 2003.
- “Computer Networking: A Top Down Approach”, 5th edition. Jim Kurose, Keith Ross Addison-Wesley, 2009.

## Slide 2: The Network Layer
IP (Internet Protocol) is a Network Layer Protocol.
RFC 791 provides the specification for IP.
Network Layer
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Send data
2. Receive data

## Slide 3: IP: The waist of the hourglass
IP is the waist of the hourglass of the Internet protocol stack.
Multiple higher-layer protocols
Multiple lower-layer protocols
One common protocol at the network layer for data transmission.

## Slide 4: Highest layer in routers
IP is the highest layer protocol which is implemented at both routers and hosts

## Slide 5: Best effort protocol
IP provides an unreliable connectionless best effort service (also called: “datagram service”).
  Unreliable: no guarantee for delivery of packets
  Connectionless: Each packet (“datagram”) is handled independently. IP is not aware that packets between hosts may be sent in a logical sequence
  Best effort: IP does not make guarantees on the service (no throughput guarantee, no delay guarantee, etc.)
Consequences: Higher layer protocols have to take care of delivery guarantees.

## Slide 6: IP Datagram
Header Size: at least 20 bytes and at most 60 bytes (with options)
Total Length: at most 216 bytes = 65536 bytes
This is IPv4

## Slide 7: IP Version
The first publicly used version of the Internet Protocol was version 4 (IPv4)
  Address space: 32 bits, (approximately 4.3 billion addresses)
  Initially it was thought to be enough!
Address exhaustion
  On February 3, 2011, the Internet Assigned Numbers Authority (IANA) officially depleted the global pool of completely fresh blocks of addresses.
  The address exhaustion was a concern as early as 1990s.
IPv6 is the next generation IP that tries to address the shortcomings of IPv4
  Has 128 bits address space
  Designed to live alongside IPv4

## Slide 8: What about VERSION 5?
It doesn't exist. It is in fact intentionally skipped to avoid confusion, or at least to rectify it.
  IP version 5 relates to an experimental TCP/IP protocol called the Internet Stream Protocol, Version 2, originally defined in RFC 1190.
  This protocol was originally seen by some as being a peer of IP at the Internet Layer in the TCP/IP architecture, and in its standard, these packets were assigned IP version 5 to differentiate them from “normal” IP packets (version 4).
  This protocol apparently never went anywhere, but to be absolutely sure that there would be no confusion, version 5 was skipped over in favor of version 6.

## Slide 9: A bit of history
“The decision to put a 32-bit address space on there was the result of a year's battle among a bunch of engineers who couldn't make up their minds about 32, 128, or variable-length. And after a year of fighting, I said--I'm now at ARPA, I'm running the program, I'm paying for this stuff, I'm using American tax dollars, and I wanted some progress because we didn't know if this was going to work. So I said: OK, it's 32-bits. That's enough for an experiment; it's 4.3 billion terminations. Even the Defense Department doesn't need 4.3 billion of everything and couldn't afford to buy 4.3 billion edge devices to do a test anyway. So at the time I thought we were doing an experiment to prove the technology and that if it worked we'd have opportunity to do a production version of it. Well, it just escaped! It got out and people started to use it, and then it became a commercial thing. So this [IPv6] is the production attempt at making the network scalable.”
-- Vint Cerf, one of the “fathers of the Internet”. (From: Google IPv6 Conference 2008)

## Slide 10: IP Datagram Fields
Version (4 bits): current version is 4, next version will be 6.
Header length (4 bits): length of IP header, in multiples of 4 bytes
DS: Type of service, or type of data (used to specify priority or request low-delay routes)

## Slide 11: IP Datagram Fields
Identification (16 bits): Unique identification of a datagram from a host. Incremented whenever a datagram is transmitted

## Slide 12: Time to live
Time To Live (TTL) (1 byte):
  Specifies longest paths before datagram is dropped
  Role of TTL field: Ensure that packet is eventually dropped when a routing loop occurs
  Used as follows:
  Sender sets the value (e.g., 64)
  Each router decrements the value by 1
  When the value reaches 0, the datagram is dropped

## Slide 13: IP Datagram Fields
Protocol (1 byte): Specifies the higher-layer protocol (e.g. TCP and UDP) for demultiplexing.
Header checksum (2 bytes): A simple 16-bit long checksum of the header

## Slide 14: The rest
Source and Destination IPs
Options:
    Security restrictions
    Record Route: each router that processes the packet adds its IP address to the header.
    Timestamp: each router that processes the packet adds its IP address and time to the header.
    (loose) Source Routing: specifies a list of routers that must be traversed.
    (strict) Source Routing: specifies a list of the only routers that can be traversed.
Padding: Padding bytes are added to ensure that header ends on a 4-byte boundary

## Slide 15: Fragment flags and offset
Flags (3 bits): First bit always set to 0, DF bit (Do not fragment), MF bit (More fragments)
Fragment offset: For fragmentation/reassembly

## Slide 16: Maximum Transmission Unit
Maximum size of IP datagram is 65535, but the data link layer protocol generally imposes a limit that is much smaller
Example:
  Ethernet frames have a maximum payload of 1500 bytes
   IP datagrams encapsulated in Ethernet frame cannot be longer than 1500 bytes
The limit on the maximum IP datagram size, imposed by the data link protocol is called maximum transmission unit (MTU)
MTUs for various data link protocols:
  -- Ethernet: 1500 -- FDDI: 4352
  -- 802.3: 1492 -- ATM AAL5: 9180
  -- 802.5: 4464 -- 802.11(WLAN): 2272

## Slide 17: IP Fragmentation
MTUs: FDDI: 4352 Ethernet: 1500
Fragmentation:
  IP router splits the datagram into several datagram
  Fragments are reassembled at receiver
What if the size of an IP datagram exceeds the MTU?
IP datagram is fragmented into smaller units.
What if the route contains networks with different MTUs?

## Slide 18: Fragmentation / reassembly
  Fragmentation can be done at the sender or at intermediate routers
  The same datagram can be fragmented several times.
  Reassembly of original datagram is only done at destination hosts !!

## Slide 19: Fields used for fragmentation
The following fields in the IP header are involved:
Identification: When a datagram is fragmented, the identification is the same in all fragments
Flags:
  DF bit is set: Should not fragment this Datagram, should be discarded if MTU is too small
  MF bit set: This datagram is part of a fragment and an additional fragment follows this one
Fragment offset: Offset of the payload of this fragment in the original datagram
Total length: Total length of the current fragment

## Slide 20: Example of Fragmentation
A datagram of 4000B from a network of 4000 MTU to 1500 MTU
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=1480
fragflag
=1
length
=1500
ID
=x
offset
=2960
fragflag
=0
length
=1040
One large datagram becomes
several smaller datagrams

## Slide 21: Resources
Slides from the book: “Mastering Computer Networks: An Internet Lab Manual”, J. Liebeherr, M. El Zarki, Addison-Wesley, 2003.
Slides from the book: “Computer Networking: A Top Down Approach”, 5th edition. Jim Kurose, Keith Ross Addison-Wesley, 2009.
RFC 791
  http://tools.ietf.org/pdf/rfc791.pdf