## Slide 1: Hubs, Switches and Bridges
University of Calgary – CPSC 441

## Slide 2: LAN Interconnection
We need to break down big networks to sub-LANs
  Limited amount of supportable traffic: on single LAN, all stations must share bandwidth
  Limited length: 802.3 (Ethernet) specifies maximum cable length. For 10 Mbps:
    Maximum length of the wire: 2,500 meter
  Large “collision domain” (can collide with many stations)

## Slide 3: HUBS
Physical Layer devices
Essentially repeaters operating at bit levels: repeat received bits on one interface to all other interfaces
Hubs can be arranged in a hierarchy (or multi-tier design), with backbone hub at its top
Each connected LAN referred to as LAN segment
twisted pair
hub

## Slide 4: Hubs: Pros and Cons
Hub Advantages:
  simple, inexpensive device
  Multi-tier provides graceful degradation: portions of the LAN continue to operate if one hub malfunctions
  extends maximum distance between node pairs (100m per Hub)
Hubs do not isolate collision domains: node may collide with any node residing at any segment in LAN
  Single collision domain results in no increase in max throughput
  multi-tier throughput same as single segment throughput
  Individual LAN restrictions pose limits on number of nodes in same collision domain and on total allowed geographical coverage
  cannot connect different Ethernet types (e.g., 10BaseT and 100baseT) Why?

## Slide 5: Bridges
Link-layer devices:
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
Advantages:
  Isolates collision domains resulting in higher total max throughput, and does not limit the number of nodes nor geographical coverage
  Can connect different type Ethernet since it is a store and forward device
  Transparent: no need for any change to hosts LAN adapters

## Slide 6: Switches
A switch could be considered a bridge with numerous ports.
Switch or Layer 2 switch is often used interchangeably with bridge
Plug-and-play, self-learning
  switches do not need to be configured

## Slide 7: Switch: allows multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ simultaneously, without collisions
  not possible with dumb hub
A’
B
B’
C
switch with six interfaces
(1,2,3,4,5,6)
1
2
3
4
5
6

## Slide 8: Switch Table
Q: how does switch know that A’ reachable via interface 4, B’ reachable via interface 5?
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?
A
A’
B
B’
C
C’
switch with six interfaces
(1,2,3,4,5,6)
1
2
3
4
5
6

## Slide 9: Switch: self-learning
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 10: Switch: frame filtering/forwarding
When frame received:
1. record link associated with sending host
2. index switch table using MAC dest address
3. if entry found for destination then {
if dest on segment from which frame arrived then drop the frame
else forward the frame on interface indicated
}
else flood
forward on all but the interface
on which the frame arrived

## Slide 11: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
frame destination unknown:
flood
A’ A
destination A location known:
A’
4
60
selective send

## Slide 12: Interconnecting switches
switches can be connected together
A
B
Q: sending from A to G - how does S1 know to forward frame destined to F via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 13: What will happen with loops?
Incorrect learning
A
B
1
1
2
2
A , 1
A , 1
2
2

## Slide 14: Spanning Trees
Allow a path between every LAN without causing loops (loop-free environment)
Bridges communicate with special configuration messages (BPDUs)
Standardized by IEEE 802.1D
Requirements:
  Each bridge is assigned a unique identifier
  A broadcast address for bridges on a LAN
  A unique port identifier for all ports on all bridges
    MAC address
    Bridge id + port number

## Slide 15: Example Spanning Tree
B3
B5
B7
B2
B1
B6
B4
Root
B8
Designated
Bridge
Root
port
Protocol operation:
Picks a root
For each LAN, picks a designated bridge that is closest to the root.
All bridges on a LAN send packets towards the root via the designated bridge.

## Slide 16: Example Spanning Tree
B3
B5
B7
B2
B1
B6
B4
Root
B8
B2
B4
B5
B7
B8
B1
Spanning Tree:
Designated
Bridge
Root
port

## Slide 17: Spanning Tree Algorithm: overview
1. Determine the root bridge among all bridges
2. Each bridge determines its root port
  The port in the direction of the root bridge
3. Determine the designated bridge on each LAN
  The bridge which accepts frames to forward towards the root bridge
  The frames are sent on the root port of the designated bridge

## Slide 18: Spanning Tree Algorithm: Selecting Root Bridge
Initially, each bridge considers itself to be the root bridge
Bridges send BDPU frames to its attached LANs
  The bridge and port ID of the sending bridge
  The bridge and port ID of the bridge the sending bridge considers root
  The root path cost for the sending bridge
Best one wins
  (lowest root ID/cost/priority)

## Slide 19: Spanning Tree Algorithm: Selecting Root Ports
Each bridge selects one of its ports which has the minimal cost to the root bridge
In case of a tie, the lowest uplink (transmitter) bridge ID is used
In case of another tie, the lowest port ID is used

## Slide 20: Select Designated Bridges Forwarding/Blocking state
Same as selecting the root brigde:
Initially, each bridge considers itself to be the designated bridge, send BDPU frames to attached LANs, best one wins!
Root and designated bridges will forward frames to and from their attached LANs
All other ports are in the blocking state

## Slide 21: Spanning Tree Protocol: Execution
B3
B5
B7
B2
B1
B6
B4
B8
(B1,root=B1, dist=0)
(B1,root=B1,dist=0)
(B4, root=B1, dist=1)
(B6, Root=B1dist=1)

## Slide 22: Switches vs. Routers
both store-and-forward devices
  routers: network layer devices (examine network layer headers)
  switches are link layer devices
routers maintain routing tables, implement routing algorithms
switches maintain switch tables, implement filtering, learning algorithms

## Slide 23: References
Parts of the slides contents are courtesy of the following people:
  Jim Kurose, Keith Ross: http://www.aw-bc.com/kurose_ross/
  Yishay Mansour: http://www.cs.tau.ac.il/~mansour/networking-course/Icc3.ppt