## Slide 1: Wi-Fi LANs
University of Calgary – CPSC 441

## Slide 2: Introduction
Wi-Fi or WiFi: defined as any "wireless local area network (WLAN) products that are based on the IEEE 802.11 standards.
Popular technology that allows an electronic device to exchange data wirelessly (using radio waves) over a computer network.
IEEE established the 802.11 Group in 1990. Specifications for standard ratified in 1997.
  Initial speeds were 1 and 2 Mbps.
  IEEE modified the standard in 1999 to include 802.11a (54 Mbps) and 802.11b (11 Mbps). Incidentally, 802.11b equipment was available before 802.11a.
  802.11g (54 Mbps) was added in 2003.

## Slide 3: The Basics
In many respects, the IEEE 802.11b wireless LAN (WLAN) standard is similar to that of classic IEEE 802.3 (Ethernet) LANs
Similarities:
  LAN with limited geographic coverage
  Multiple stations, with 48-bit MAC addresses
  Shared transmission medium (broadcast technology)
  CSMA-based Medium Access Control protocol
  Comparable data rates (11 Mbps vs 10 Mbps)

## Slide 4: The Basics
But there are also many distinct differences:
  Wireless (air interface) versus wired (coax)
  Wireless propagation environment (multipath)
  Higher error rate due to interference, fading, etc.
  Successful frames are ACKed by receiver
  Mobile stations versus fixed stations
  Half-duplex versus full-duplex operation
  “Hidden node” and “exposed node” problems (exposed node problem occurs when a node is prevented from sending packets to other nodes due to a neighboring transmitter.)
  Potential asymmetries of links
  CSMA/CA versus CSMA/CD
  Multiple data transmission rates (1, 2, 5.5, 11)

## Slide 5: Some Wi-Fi Features
Infrastructure mode vs “ad hoc” mode:
  Devices in a wireless network are set up to either communicate indirectly through a central place — an access point — or directly, one to the other.
Access Point (AP) sends “beacon frames” – all the information about the network (e.g. Timestamp Capability information)
  Mobiles choose AP based on signal strength
Multiple channel access protocols supported
  CSMA/CA (DCF – Distributed coordination function); PCF (Point Coordination Function); RTS/CTS (Request to Send/Clear to Send)

## Slide 6: Other Wi-Fi Features
MAC-layer can provide error control, retransmission, rate adaptation, etc.
Direct Sequence Spread Spectrum (DSSS)
  Modulation technique
  Signal spread across 22 MHz with each channel based around a center frequency. There are fourteen 22-MHz channels.

## Slide 7: Where Does Wireless RF Live?
ISM (Industrial, Scientific, Medical) Band
902-928 MHz | 2.4 – 2.5 GHz | 5.725 – 5.875 GHz | 24 – 24.250 GHz | 57 – 66 GHz
802.11-1997 | 802.11b/g/n | 802.11a/n/ac |  | 802.11ad
Cordless Phones | Cordless Phones |  | Amateur Satellite | 
Baby Monitors | Baby Monitors |  |  | 
 | Bluetooth |  |  | 
 | Microwave Ovens |  |  | 

## Slide 8: Protocol Stack View
Application | Telnet, FTP, Email, Web
Transport | TCP, UDP, SCTP
Network | IPv4, IPv6
Data Link | 802.3 (Ethernet) MAC, 802.11 (Wi-Fi) MAC, DOCSIS, ISDN
Physical | Copper LAN: 10/100/1000/10G/40GBASE-T Fiber LAN: 10GBASE-SR/LR/ER Wireless LAN: FHSS, DSSS, IR
Wi-Fi occupies layers 1 & 2 only!

## Slide 9: Wireless Cells
In Canada/US, there are eleven 802.11b/g channels
Only channels 1, 6 and 11 are non-overlapping
Computers can roam between cells
11 Mbps bandwidth
“shared” by all devices
in the Cell!
Access Point coverage
area is called a “Cell”
Range per Access Point is 100m
Access Point Channel 6 ESSID: NAI

## Slide 10: Multiple Wireless APs
1
6
11
1
1
11

## Slide 11: Medium Access Control (MAC)
Carrier Sense Multiple Access with Collision Avoidance (CSMA-CA)
  Device wanting to transmit senses the medium (air)
  If medium is busy, it defers
  If medium is free for certain period (DIFS – Distributed Inter-Frame Space), it transmits frame
  DIFS is approximately 128 µs
  Latency can increase if “air” is very busy since devices will have a hard time finding “open air” to send frames!

## Slide 12: MAC Protocol
DIFS – Distributed Inter-Frame Space (approx. 128 µs)
SIFS – Short Inter-Frame Space (approx. 28 µs)
Every frame is ACKed except broadcast/multicast
“Air” is free
for DIFS time
period
Receive ACK back
that frame was
received intact!
send frame
source
destination
others
DIFS
SIFS
All other devices
must defer while “air” is busy
data
ack
NAV: defer access

## Slide 13: MAC Retransmission
If no ACK received “right away”, then the sender retransmits the frame again at the MAC layer
  indicates frame (or ACK) was lost/corrupted
  very short timeout (e.g., 1 ms)
  exponential back off (doubling) if repeated loss
Typically recovers before TCP would notice
Max retransmission limit (e.g., 8)
May do MAC-layer rate adaptation or frame fragmentation if channel error rate is high

## Slide 14: Other MAC Protocols Supported
Point Coordination Function (PCF)
  AP polls stations in turn to see if there’s frames to send
  useful for real-time traffic
Request-To-Send/Clear-To-Send (RTS/CTS)
  reservation-based approach (ask permission)
  useful for very large frames
  useful for solving the “hidden node” problem (when a node is visible from a wireless access point (AP), but not from other nodes)
  request asks for clearance (permission) to send
  request also indicates time required for transmit

## Slide 15: Frame Formats
Two frame formats available:
  long preamble
  short preamble
Configuration option for NIC (Network interface controller) and AP
Variable-size frames (maximum of 2312 bytes for payload)
16-bit Cyclic Redundancy Code (CRC) for error checking of frames

## Slide 16: Long Preamble
Long Preamble = 144 bits
  Interoperable with older 802.11 devices
  Entire Preamble and 48 bit PLCP (Physical Layer Convergence Protocol) header sent at 1 Mbps
128 bit Preamble
(Long)
16 bit
Start
Frame
Delimiter
Signal Speed
1,2,5.5,11
Mbps
Service
(unused)
Length
of
Payload
16 bit
CRC
Payload
0-2312 bytes
Transmitted at 1 Mbps
Transmitted at X Mbps

## Slide 17: Short Preamble
Short Preamble = 72 bits
  Preamble transmitted at 1 Mbps
  PLCP (Physical Layer Convergence Protocol) header transmitted at 2 Mbps
  More efficient than long preamble
56 bit
Preamble
Payload
0-2312 bytes
Transmitted
at
1 Mbps
16 bit
Start
Frame
Delimiter
Signal Speed
1,2,5.5,11
Mbps
Service
(unused)
Length
of
Payload
16 bit
CRC
Transmitted
at
2 Mbps
Transmitted
at
X Mbps

## Slide 18: More Features
Power Management
  Mobile nodes can “sleep” to save power
    Accomplished by using DTIM (Delivery Traffic Indication Message) intervals
  AP will buffer frames until client requests them
  AP can use virtual bitmap field in beacons to indicate which stations have data waiting
Security
  Wired Equivalent Privacy (WEP)
    Not very secure at all!
  To address this weakness, there is WPA2 (IEEE 802.11i)
    Uses CCMP, an AES-based encryption mode with strong security