## Slide 1: Asynchronous Transfer Mode: An Introduction
Carey Williamson
Department of Computer Science
University of Calgary

## Slide 2: ATM: What it is
Asynchronous Transfer Mode
A low-layer networking technology (aspects of Network/Datalink Layers) based on fast packet-switching of small fixed size packets called cells
ATM provides a single transport mechanism for integrated services traffic: data, voice, video,...
All statistically multiplexed at ATM layer, with transmission slots assigned on an “on demand” basis

## Slide 3: Asynchronous Transfer Mode (1of2)
About 20 years old
Packet-switched network
Small fixed-size packets (53 bytes)
Designed for integrated services (voice, video, data, imaging, interactivity,…)
High speed network technologies (optical)
Wide range of user and application behaviour
Bursty, variable bandwidth required per call
Aggregation of traffic at switches
Transmission links shared on a stat mux basis

## Slide 4: ATM (2 of 2)
Connection-oriented
Allocates a virtual channel (VC) per active call
End to end path allocation determined at time of call arrival; reserved bandwidth per active call
All packets travel same path (order preserved)
Crucial state info in ATM switches
Bundles of related VC’s handled via Virtual Path (VP)
5-byte header (VPI and VCI) plus 48-byte payload
An example of “label switching” at NL/DL layers
Multiple classes of service (priority levels)
Offers end to end QOS guarantees (SLAs)

## Slide 5: ATM Cell Format
53 bytes
5 byte header
48 byte payload (data)
Virtual Path Identifier (VPI)
Virtual Channel Identifier (VCI)
Simple control fields

## Slide 6
ATM Cell Format
GFC
VPI
Payload
(48 bytes)
VPI
VCI
VCI
HEC
PT
CLP
VCI
ATM UNI Cell Specification
RES