## Slide 1: Congestion Control in SDN-Enabled Networks
Carey Williamson
Department of Computer Science
University of Calgary

## Slide 2: Introduction and Motivation
There is a new emerging suite of high-bandwidth Internet apps based on interactive video
  Example 1: 360-degree video
  Example 2: Cloud-based gaming services
  Example 3: JPEG 2000 Interactive Protocol (JPIP)
Challenges:
  High bandwidth requirements for interactive video
  Latency sensitivity for remote user interactions
  Need to support multiple service classes
  Overhead of resource reservation mechanisms
  Limited effectiveness of end-to-end congestion control

## Slide 3: This Paper
Research Question: Can SDN provide effective and responsive congestion control for these applications?
Answer: Yes!
Proposed Solution:
  Network-exposed API for network state visibility
  SDN-assisted congestion control with low latency, high bw
  Fair sharing between interactive and non-interactive flows
Extensive evaluation of effectiveness and scalability
A. Naman, Y. Wang, H. Gharakheilia, V. Sivaraman, and D. Taubman,
“Responsive High Throughput Congestion Control for Interactive Applications
over SDN-Enabled Networks”, Computer Networks, April 2018.

## Slide 4: System Architecture

## Slide 5: Exposing Network State Information
RESTful API (HTTP-based)
Registration required by interactive flows
Network query response protocol for state info
Request format:
  GET /stats/<MyIP>/<PeerIP>/<LastIdx>/<MaxEntr>/
Response format:
  Network state entries: [ns entry1; ns entry2; …]
  Link state entries: [i, L, link_entry1, link_entry2, …]
  Information and format: [delta_i, b_i, q_i, R_i, d_i]

## Slide 6: Control Algorithm
Two queues: interactive and non-interactive
Dynamic estimation of number of bytes queued at the bottleneck point on an end-to-end path
Try to limit this queue size for interactive traffic
Formulas derived for control-theoretic dynamics
Analogous to “Rate-Delay (RD) Network Services” by M. Podlesny and S. Gorinsky, ACM SIGCOMM 2008

## Slide 7: Experimental Evaluation
Experimental setup with Mininet

## Slide 8: Experimental Results (1 of 12)
Figure 3: Average Bandwidth (Mbps) versus Time

## Slide 9: Experimental Results (2 of 12)
Figure 4: Bottleneck Queue Size (bytes) vs Time

## Slide 10: Experimental Results (3 of 12)
Figure 5: Video Quality (PSNR) versus Time (frames)

## Slide 11: Experimental Results (4 of 12)
Figure 6:
Multiple Flows

## Slide 12: Experimental Results (5 of 12)
Figure 7: Bandwidth and Queued Bytes vs Time

## Slide 13: Experimental Results (6 of 12)
Figure 8:
(a) Throughput vs Time
(b) RTT vs Time
(c) PSNR vs Time

## Slide 14: Experimental Results (7 of 12)
Figure 9:
(a) Num Flows vs Time
(b) Available Bandwidth vs Time
(c) Throughput vs Time

## Slide 15: Experimental Results (8 of 12)
Figure 10:
(a) RTT vs Time
(b) Avg Queued Bytes vs Time
(c) PSNR vs Time

## Slide 16: Federated Network Scenario

## Slide 17: Experimental Results (9 of 12)
Figure 12: Bandwidth and Queued Bytes vs Time

## Slide 18: Experimental Results (10 of 12)
Figure 13:
(a) Bandwidth vs Time
(b) Queued Bytes at P1
(c) Queued Bytes at P2

## Slide 19: Experimental Results (11 of 12)
Figure 14:
(a) Bandwidth vs Time
(b) Queued Bytes at P1
(c) Queued Bytes at P2

## Slide 20: Experimental Results (12 of 12)
Figure 15:
(a) Bandwidth vs Time
(b) Queued Bytes at P1
(c) Queued Bytes at P2

## Slide 21: Conclusions
SDN-assisted congestion control can provide the responsiveness needed for interactive video apps
Key idea is to expose and exploit network state info
Experimental results show that the proposed approach is responsive and fair, even in the presence of highly dynamic network flows
Future work:
  More efficient protocols for streaming network state info
  More effective solutions for high-latency federated networks